# BARREL SAND FILTER

Conducting Maintenance

Maintenance is required when the rate of water flow slows down too much.  At this point, the following steps are required:

- Remove the lid and the colander/diffuser basin.

- Lower the water level inside the filter by using a small cup to scoop out the water that has not drained through the outlet pipe.

- Make a small hole in the sand with the cup.  Scoop out the water that accumulates in it until only wet sand remains.

- Remove 3 to 5cm of the fine sand layer and set it aside.  (After washing and drying in the sun, this sand may be reused next time maintenance is performed.)

- Reinstall the colander/diffuser basin.

- Slowly add water to the filter until water begins to flow through the outlet pipe again.

- Again remove the colander/diffuser basin and add clean, fine sand until the layer of sand reaches a level of 5cm below the water surface.  Level the surface of the sand.

- Reinstall the colander/diffuser basin and the lid.

The filter is ready to be used again.  Its normal operation will be reestablished after 2 to 3 days.